## Slide 1: PolyRhythm: Adaptive Tuning of a Multi-Channel Attack Template for Timing Interference
Ao Li*, Marion Sudvarg*,
Han Liu, Zhiyuan Yu, Chris Gill, Ning Zhang
RTSS 2022
* Presenters and Equal Contributions

## Slide 2: Motivation
Multi-core computing platforms
  Improved performance
  Better for size, weight and power (SWaP) constraints
  Increasingly deployed on embedded real-time systems

## Slide 3: Motivation
Interference is a long-standing problem
  Shared resource contention by co-running tasks
  Worst-case performance is unpredictable
  Malicious interference can cause hundreds of times of delay
  Characterizing interference in complex systems is challenging
How can we, as system designers, empirically profile worst-case/malicious interference?

## Slide 4: Survey on Existing Literature
VFS
File Systems
Volume Manager
Socket
SK_buffer
TCP/UDP
Context Switching
Task Scheduling
Device Driver
CPU Port
Row Buffer
Cache
TLB
System Call Interface
Task Spawning
Bus
Usenix Security' 07
RTAS' 22
RTAS' 20
PACT' 15
RTAS' 19
OS Review' 08
OSDI' 10
CCS' 12
Usenix ATC' 11
ISCA' 14
RTAS' 20
ISCA' 16
S&P' 19
ISCA' 19
RTSS' 11
SIGMETRICS' 13
Asia CCS' 17
RTAS' 15
OSDI' 20
DAC' 01
EMSOFT' 12
ASPLOS' 10
OS-based Channels
Architectural Channels

## Slide 5: Survey on Existing Literature
VFS
File Systems
Volume Manager
Socket
SK_buffer
TCP/UDP
Context Switching
Task Scheduling
Device Driver
CPU Port
Row Buffer
Cache
TLB
System Call Interface
Task Spawning
Bus
OS-based Channels
Architectural Channels

## Slide 6: Research Challenges
What are the resource-contention channels?
How do we automatically tune the parameters for diverse and heterogenous OSes and architectures?
How can we adaptively select combinations of different channels to maximize the attack impact?

## Slide 7: Overview of Our Proposed Solution
Systemization of performance interference on:
  Shared OS resources
  Shared architectural resources
Automatic tuning of maximum performance interference on each channel (Platform-targeted)
Adaptive combination of different channels to maximize the attack effects (Workload-targeted)
We want to enable design of more resilient systems
                Characterizing worst-case/malicious multi-channel timing interference

## Slide 8: PolyRhythm
A templated tool for running worst-case/maximum interference
  Synthesizes primitives across multiple architectural and kernel-based channels
  Uses a genetic algorithm to tune platform-specific parameters offline
  Searches online to find contention regions
  Reinforcement learning dynamically selects which channel to target online at each time step

## Slide 9: Threat Models and Isolation
(a) Core Partitioning
(b) Low-Priority Attacker
(c) Bandwidth Limitations

## Slide 10: Cache Channels
Potential sources of interference:
  Cache evictions on common core
  Shared last level cache
  Shootdowns on shared TLB
Cache coloring or partitioning can help
But there may be hidden shared resources
  Miss status holding registers
  Writeback buffer
./polyrhythm cache <threads> <stride> <size>
Attack Cache
Allocate array of size
Iteration step in cache lines
(TLB primitive parameters available in online manual)
Number concurrent attack threads

## Slide 11: Memory Channels
Contention for common memory controller and bus
DRAM Row
Buffer
Data in DRAM row buffers returned significantly faster
Attempt to evict victim data from buffers
./polyrhythm row_buffer <threads> <stride> <size> <pattern>
Attack DRAM row buffer
Allocate array of size
Random or sequential access
(Memory bandwidth primitive parameters available in online manual)
Number concurrent attack threads
Sequential iteration step

## Slide 12: OS Channels
I/O Attack Primitives
  Network and block devices are increasingly fast
  I/O request queues are getting larger, increasing contention
  I/O scheduler can be targeted for overhead
  Contention points along deep driver stacks may be exploited
File System Attack
  Locked data structures can cause priority inversion
Fork Bomb Attack
  Increase size of queues and endpoints
  Overwhelm thread structure allocators
(All 9 channel primitive parameters available in online manual)

## Slide 13: Genetic Algorithm for Offline Tuning
For each primitive, find best parameters for target platform (Arch+OS)
Run against a workload that heavily uses the channel
Use hardware performance counters to determine effectiveness
Each generation, try several sets of parameters
GA/main.py
Independently tune all channels
--channel cache
Tune only cache channel
Next generation crosses parameters from most successful previous runs
Performed offline
  No prior knowledge of victim workloads
  Allows access to hardware performance event counters

## Slide 14: Online Contention Region Search
Resource locality and runtime allocation may be variable
  Hardware page mapping locality based on availability
  Binding open network ports at launch
PolyRhythm’s online attack can search for regions overlapping with victim
  Cache eviction sets
  Common DRAM rows
  Network ports and address families
Profiles its own execution times to infer interference
  No elevated privileges required for online attack
Regions not highly dynamic across victim lifetime
  Real-time tasks often avoid dynamic paging
  Port numbers remain consistent
Fast
Slow
./polyrhythm cache <threads> <stride> <size> <online:0/1>

## Slide 15: Dynamic Spatio-Temporal Primitive Selection
At each time step select the primitive that maximizes victim delays
Different victim workloads have different control flows and resource usage patterns
PolyRhythm uses reinforcement learning to select action
Train a deep deterministic policy gradient using hardware-in-the-loop against target platform running representative victim application
Trained action network loaded with online attacker

## Slide 16: Effect of Offline Tuning
Compared PolyRhythm’s tuned cache primitive to untuned BWWrite attack from:
M. Bechtel and H. Yun, “Denial-of-service attacks on shared cache in multicore: Analysis and prevention.” RTAS 2019
CortexSuite benchmark victim running on dedicated core
Captured mean slowdowns over 100 runs
X Slowdown
Platform: Raspberry Pi 3B

## Slide 17: Attack Primitive Platform Dependence
Compared tuned primitives on multiple platforms
Victims selected from stress-ng workloads
Victim runs on dedicated core
Measured max slowdown over 100 runs
X Slowdown
Platform: Intel Nuc 8

## Slide 18: Attacking ORB-SLAM3
Attack ORB-SLAM3 on Intel Nuc
Running with 50ms main loop over EuRoC MAV dataset
We compare slowdowns induced by PolyRhythm’s multiple stages
HyperThreading Enabled
ORB-SLAM3 high priority
PolyRhythm low priority
8 attack threads
No Attacker

## Slide 19: Attacking ORB-SLAM3
Attack ORB-SLAM3 on Intel Nuc
Running with 50ms main loop over EuRoC MAV dataset
We compare slowdowns induced by PolyRhythm’s multiple stages
HyperThreading Enabled
ORB-SLAM3 high priority
PolyRhythm low priority
8 attack threads
Cache Attack
Overrun

## Slide 20: Attacking ORB-SLAM3
Attack ORB-SLAM3 on Intel Nuc
Running with 50ms main loop over EuRoC MAV dataset
We compare slowdowns induced by PolyRhythm’s multiple stages
HyperThreading Enabled
ORB-SLAM3 high priority
PolyRhythm low priority
8 attack threads
Online Contention
Region Search
Overrun

## Slide 21: Attacking ORB-SLAM3
Attack ORB-SLAM3 on Intel Nuc
Running with 50ms main loop over EuRoC MAV dataset
We compare slowdowns induced by PolyRhythm’s multiple stages
HyperThreading Enabled
ORB-SLAM3 high priority
PolyRhythm low priority
8 attack threads
Dynamic Spatio-Temporal Primitive Selection
Overrun

## Slide 22: Conclusions
PolyRhythm demonstrates the ability of targeted attacks to substantially inflate execution times
May inform more accurate WCET estimates
Helps to analyze the effectiveness of isolation techniques
Open source and available to all:
https://github.com/WUSTL-CSPL/PolyRhythm
We welcome engagement from the community: questions, collaboration, and contributions

## Slide 23: Thank You!
Any Questions?
QR Code:
Project Link:
https://github.com/WUSTL-CSPL/PolyRhythm